## Slide 1: TLS NXAPI and Openflow scripts

## Slide 2: What is supported?
Switch mode |  |  |  | 
NXAPI | Single NDB and Single switch | Single NDB and multiple switches | Multiple NDB and single switch | Multiple NDB and multiple switches
Openflow | Single NDB and Single switch | Single NDB and multiple switches | Multiple NDB and single switch | Multiple NDB and multiple switches

## Slide 3: What is supported?
All controllers should have the same HA clustering configuration information in the config.ini files
In HA mode the information which is provided in first block of input file will be treated as Master .Remaining servers will be treated as a Slaves.
Restriction for NXAPI
We can connect maximum 10 devices at a time.

## Slide 4: TLS NXAPI and Openflow
TLS Configuration Tool will configure NXAPI/Openflow in TLS mode according to user Requirements. Using this tool Cisco Nexus Data Broker will be configured with the required certificates and it should be started in the secure mode. When Cisco Nexus Data Broker is started in TLS mode, all devices will be connected in secure mode.

## Slide 5: TLS Script - Prerequisites
Ensure that OpenSSL is installed on the Linux host
Python
sudo apt-get install python2.7
Pip
sudo apt-get -y install python-pip
pexpect
pip install pexpect
yaml
pip install pyyaml
requests
pip install requests
paramiko
sudo apt-get install python-paramiko

## Slide 6: TLS NXAPI Script usage
Clone the code from the below link.
git clone https://github.com/datacenter/nexus9000.git
Navigate to following path:
cd nexus9000/
cd nexusdatabroker/
cd TLSNXAPITool1.0/
Run python script using following command :
python TLSNXAPITool.py

## Slide 7: TLS NXAPI Script Input and Logs
The input file is present in corresponding path –
TLSNXAPITool1.0/Utilities/Input/inputfile.yaml
IP:
IP1:
port: 443 # can be any port number
address: 10.16.206.127
username: admin
password: cisco123
ServerIP:
ServerIP1: # Can give any number of servers
ip: 10.16.206.179
user: root
password: cisco123
path_ndb_build: /root/Ndb3.2-Releasebuild/xnc/configuration # NDB build path to be given till xnc folder

## Slide 8: TLS NXAPI Script Input and Logs
The key value should be mentioned as following :Certificates will be generated using provided key value
Key_Password: 'cisco123'
In order to change values provide corresponding information for following fields.
If info not provided for following fields by default certificates will be generated using following values.
commonName_default = www.cisco.com
0.organizationName_default = Cisco
localityName_default = San Jose
stateOrProvinceName_default = CA
countryName_default = US
emailAddress_default = webmaster@cisco.com
organizationalUnitName_default = NDB
By default Input file consists 2 servers and 2 devices info
If tool is using for following combination and 2nd server and 2nd device details should be commented out.

## Slide 9: NXAPI TLS Script Logs
The logs can be seen in following way.
After running python script using following command :
python TLSNXAPITool.py
Log file generated - TLSNXAPITool1.0/Utilities/Log/Logfile.log

## Slide 10: Openflow TLS script usage
Clone the code from the below link.
git clone https://github.com/datacenter/nexus9000.git
Navigate to following path:
cd nexus9000/
cd nexusdatabroker/
cd TLSOPENFLOWTool1.0/
Run python script using following command :
python TLSScriptOF.py

## Slide 11: Openflow TLS script Input and Logs
The input file is present in corresponding path –
TLSOPENFLOWTool1.0 /Utilities/Input/inputfile.yaml ( This can be changed according to server/switch used same as NXAPI)
IP:
IP1: # Can give any number of devices
address: 10.16.206.116
username: admin
password: cisco123
ServerIP:
ServerIP1: # Can give any number of servers
ip: 10.16.206.160
user: root
password: cisco123
path_ndb_build: /root/Ndb3.3-Releasebuild/xnc # NDB build path to be given till xnc folder

## Slide 12: TLS Openflow script Input and Logs
Log file generated - TLSOPENFLOWTool1.0 /Utilities/Log/Logfile.log
Once python runs successfully add openflow controller to NDB .If NDB is running in HA(Cluster) mode add all openflow controllers to NDB .
Steps -
FOR NXOS below I5 version
switch(config)# openflow
switch(config-ofa)# switch 1
switch(config-ofa)# tls trust-point local myCA remote myCA
switch(config-ofa-switch)# pipeline{201/203}
switch(config-ofa-switch)#controller ipv4 {A.B.C.D} port 6653 vrf management security tls
FOR NXOS above I5 version
switch(config)# openflow
switch(config-ofa)# switch 1 pipeline 201
switch(config-ofa)# tls trust-point local myCA remote myCA
switch(config-ofa-switch)#controller ipv4 {A.B.C.D} port 6653 vrf management security tls

## Slide 13: Limitations
Only self signed TLS certificate is supported.
Script is tested on Ubuntu server currently.
Known caveats
CSCvf07022 | Created certificates and files are still present Once script terminates in middle of execution